## Slide 1: Automated Vehicle Interaction with Pedestrians
PIs:
Lionel P. Robert Jr. (School of Information, UM-Ann Arbor)
Dawn M. Tilbury (Mechanical Engineering, UM-Ann Arbor)
Xi (Jessie) Yang (Industrial and Operations Engineering, UM-Ann Arbor)
Anuj K. Pradhan (Mechanical and Industrial Engineering, Umass-Amherst)
Student: Suresh Kumaar Jayaraman (Mechanical Engineering, UM-Ann Arbor)

## Slide 2: Motivation
Crossing Behavior
Long-term predictions
Multiple future prediction (multi-modal)
Computational efficiency
Explainability

## Slide 3: Related Work
Physics-based
Planning-based
Pattern-based
  Neural Networks
    Deep learning

## Slide 4: Research Questions
How is pedestrian crossing behavior influenced by the implicit driving behavior of the AVs?
How best to represent pedestrian behavior suited for AV planning applications?
How does interaction between multiple agents influence the predictions?

## Slide 5: Hybrid Framework – Probabilistic Hybrid Automata
Notes: For capturing both long-term and short-term pedestrian dynamics, I am proposing a hybrid framework where each possible pedestrian action is a discrete state with probabilistic transition between the states.

## Slide 6: Hybrid Framework – Current Focus
Define continuous dynamics model
Discrete state probabilistic classification model
  Summary Stats
    Logistic Regression
  Gap acceptance Probability distribution
  Time Series
    ARMA
    Neural Network
    RNN - LSTM
Notes: For capturing both long-term and short-term pedestrian dynamics, I am proposing a hybrid framework where each possible pedestrian action is a discrete state with probabilistic transition between the states.

## Slide 7: Proposed model – short term dynamics with Noise
Assumption: Pedestrian velocity remains constant when walking
Assumption: Gaussian Noise for continuous states
Notes: The steps for hybrid model includes defining the motion models within each of the discrete state and defining the model to calculate the discrete state transitions.
Consider a constant velocity model for each of the three moving states – approach, cross, and walkaway and a constant position model for the wait state.
Each discrete state is assumed to have fixed target that is obtained from the map of the environment and the velocity and heading are fixed based on initial observations and target and updated based on measurements.

## Slide 8: Proposed model – short term dynamics with Noise
Assumption: Pedestrian velocity remains constant when walking
Assumption: Gaussian Noise for continuous states
Change the dynamics – Cartesian velocity
Notes: The steps for hybrid model includes defining the motion models within each of the discrete state and defining the model to calculate the discrete state transitions.
Consider a constant velocity model for each of the three moving states – approach, cross, and walkaway and a constant position model for the wait state.
Each discrete state is assumed to have fixed target that is obtained from the map of the environment and the velocity and heading are fixed based on initial observations and target and updated based on measurements.

## Slide 9: Proposed prediction model – long term dynamics
History of discrete states, continuous states and features
Sequence of probabilities of discrete states
Inputs
Output
Probabilistic Classifier
Features would include vehicle dynamics, interaction parameters, traffic characteristics and pedestrian dynamics
Discrete State transitions (long-term behavior)
Mean of observations
Notes: For predicting the long-term dynamics, I am using the state of the art Recurrent Neural Network framework called Long Short Term Memory. The model is capable of using time-series inputs to learn temporal relationship between the inputs and give accurate predictions. Since crossing is a time-dependent activity, this model is suitable for predicting crossing trajectories.
Possible inputs include the history of pedestrian dynamics, the vehicle dynamics, traffic characteristics and other interaction cues. The model output the transition probability of the discrete states

## Slide 10: Proposed prediction model – long term dynamics
Discrete states, continuous states and features at instances when gap is evaluated
Sequence of probabilities of discrete states
Inputs
Output
Probabilistic Classifier
Features would include vehicle dynamics, interaction parameters, traffic characteristics and pedestrian dynamics
Discrete State transitions (long-term behavior)
Notes: For predicting the long-term dynamics, I am using the state of the art Recurrent Neural Network framework called Long Short Term Memory. The model is capable of using time-series inputs to learn temporal relationship between the inputs and give accurate predictions. Since crossing is a time-dependent activity, this model is suitable for predicting crossing trajectories.
Possible inputs include the history of pedestrian dynamics, the vehicle dynamics, traffic characteristics and other interaction cues. The model output the transition probability of the discrete states

## Slide 11: Classifier variants
Based on input type
  Summary statistics
  Actual time series values
Based on observation window
  Rolling window & fixed window size (= 3.2 s, similar to Alahi et al. (2016)); window grows from zero till it reaches
  Rolling window & varying window size until ; window resets and starts from zero when a vehicle gap starts
  Distinct windows based on vehicle gaps; window grows from zero when a gap starts till that gap ends

## Slide 12: Pedestrian Features/Observations
Features | Description | Type
Pedestrian Position [m] |  | Continuous
Pedestrian Speed [m/s] |  | Continuous
Pedestrian distance to curb [m] | This refers to the y-distance between pedestrian and edge of sidewalk | Continuous
Pedestrian distance to crosswalk [m] | Distance between pedestrian position and closest | Continuous
Cumulative Waiting time [s] | Time elapsed from start of waiting | Continuous
Gaze at Vehicle | Proportion of time looking a | Categorical – Yes/No
Approach Direction | Same direction as the AV or opposite direction | Categorical – Same/Opposite
Pedestrian-Vehicle distance [m] | These two together, give the time gap | 
Vehicle instantaneous speed [m/s] |  | 

## Slide 13: Vehicle Features/Observations
Features | Description | Type
Vehicle Position [m] |  | Continuous
Vehicle Speed [m/s] |  | Continuous
Vehicle Acceleration [m/s2] |  | Continuous
Distance between vehicles in same lane [m] |  | Continuous
All four vehicles
  Close and next in both lanes
Interaction Features
Features | Description | Type
Vehicle to pedestrian distance [m] |  | Continuous
Time to Collision [s] | Veh-ped distance/instantaneous vehicle speed | Continuous

## Slide 14: Summary Statistics of entire observation interval
Wait gap duration: t2-t1
Features | Description | Type
Gaze Ratio | Proportion of time looking at vehicle | Continuous
Gap duration [s] |  | Continuous
Cross gap duration: (t2-t1) + (dpv/vv)

## Slide 15: Interval Format - 1
Vehicle ‘k’ crosses pedestrian
Cross gap
Events timeline
Approach action
Wait Action
Vehicle ‘k+1’ crosses pedestrian
Vehicle ‘k+2’ crosses pedestrian
Vehicle ‘k+3’ crosses pedestrian
Vehicle ‘k+N’ crosses pedestrian
Approach starts after picking up ball/drop ball and returning
Wait starts when v~=0
Starts to cross
Intervals splits based on vehicle gaps for calculating the other observations
Considers interaction with each vehicle separately
Wait gap
Wait gap
Wait gap

## Slide 16: Input for training the Cross from Wait decision logistic regression models
Initial plan: Mean of parameters of the gap interval
Easy to train; more discriminative power

## Slide 17: Results – Cross from Wait decision
Features | Accuracy of identifying cross/wait gaps
All features | 94%
Gap duration, veh-ped distance, veh speed, veh acc, veh-veh distance | 94%
Minimal set - Gap duration, veh-ped distance, veh speed, veh acc, | 93%
Real time evaluation
Mean of parameters from cumulative observation window that resets after each gap
Accuracy (1 subject data) – 61%
  Class discrimination mainly based on vehicle parameters
  Similar vehicle parameters for wait/cross classes at the start of the gap; but model learned to discriminate for entire gap observations
Conclusion
Real time evaluation with model trained on mean of entire gap not accurate

## Slide 18: Approaches in Literature
Gap acceptance (Logistic Regression)
  Model trained on age, gender, waiting time, vehicle speed at start of gap, pedestrian-vehicle distance at start of gap, expected gap (or time-to-collision) at start of gap
  Probability of acceptance/reject evaluated at the start of the gap
  Sun et al. (2002), Fitzpatrick et al. (2006)
Action classification (Neural Networks, SVM, etc.) – Approach 1
  Concatenated time series data (fixed time steps, around 1 s) for both training and evaluation
  Action labels based on final output of that time series data (Cross/Wait)
  Volz et al. (2016), Fang et al. (2018)

## Slide 19: Currently trying: Interval Format - 2
Vehicle ‘k’ crosses pedestrian
Cross gap
Events timeline
Approach action
Wait Action
Vehicle ‘k+1’ crosses pedestrian
Vehicle ‘k+2’ crosses pedestrian
Vehicle ‘k+3’ crosses pedestrian
Vehicle ‘k+N’ crosses pedestrian
Approach starts after picking up ball/drop ball and returning
Wait starts when v~=0
Starts to cross
Intervals splits based on vehicle gaps
  Sliding window within each gap
  Final label of that gap given to each sliding window observation within that gap
Considers interaction with each vehicle separately
Wait gap
Wait gap
Wait gap

## Slide 20: Currently trying: Interval Format - 3
Fixed observation history
  1 s (0.1 s sample time)
  3.2 s (0.4 s sample time, similar to Alahi et al. (2016))

## Slide 21: Currently trying: Data format
Actual time series observations
Mean of time series observations

## Slide 22: References
Alahi, A., Goel, K., Ramanathan, V., Robicquet, A., Fei-Fei, L., & Savarese, S. (2016). Social LSTM: Human Trajectory Prediction in Crowded Spaces. In Proceedings of the IEEE conference on computer vision and pattern recognition (pp. 961–971).
Fang, Z., & López, A. M. (2018, June). Is the pedestrian going to cross? answering by 2d pose estimation. In 2018 IEEE Intelligent Vehicles Symposium (IV) (pp. 1271-1276). IEEE.
Völz, B., Behrendt, K., Mielenz, H., Gilitschenski, I., Siegwart, R., & Nieto, J. (2016, November). A data-driven approach for pedestrian intention estimation. In 2016 IEEE 19th International Conference on Intelligent Transportation Systems (ITSC) (pp. 2607-2612). IEEE.
Brewer, M., Fitzpatrick, K., Whitacre, J., & Lord, D. (2007). Exploration of Pedestrian Gap-Acceptance Behavior at Selected Locations. Transportation Research Record: Journal of the Transportation Research Board, 1982, 132–140. https://doi.org/10.3141/1982-18
Yannis, G., Papadimitriou, E., & Theofilatos, A. (2013). Pedestrian gap acceptance for mid-block street crossing. Transportation Planning and Technology, 36(5), 450–462. https://doi.org/10.1080/03081060.2013.818274
Sun, D., Ukkusuri, S. V, & Benekohal, R. F. (2002). Modeling of motorist-pedestrian interaction at uncontrolled mid-block crosswalks. Transportation Research Record, Urbana, 51(November 2002), 61801.

## Slide 23: Results - Approach to Cross/Wait classifier
Evaluated at 1.5 m from crosswalk
Gaze ratio for last 1s
SVM with Fine Gaussian gives better F1 Score

## Slide 24: Results - Approach to Cross/Wait classifier
KNN better F1 Score
Evaluated at 1.0 m from crosswalk
Gaze ratio for last 1s

## Slide 25: Results – Pedestrian Behavior
Waiting time

## Slide 26: Results – Pedestrian Behavior
Waiting time outliers

## Slide 27: Results – Pedestrian Behavior
Crossing speed

## Slide 28: Results – Pedestrian Behavior
Gap acceptance

## Slide 29: Results – Pedestrian Behavior (Learning)
Crossing speed over time

## Slide 30: Results – Pedestrian Behavior (Learning)
Waiting time over time

## Slide 31: Results – Pedestrian Behavior (Learning)
Gap acceptance over time

## Slide 32: Results - Transition
sc

## Slide 33: SVM
All 9 features

## Slide 34: SVM – Medium Gaussian
All 9 features
UnNormalized

## Slide 35: Logistic Regression
All 9 features
UnNormalized

## Slide 36: Feature Selection - Normalized
Removing Pedestrian Heading | Slightly increased accuracy (90.3%) using Ensemble; similar in other classifiers
Removing LaneID | Slightly increased accuracy using Ensemble; similar in other classifiers
Removing GazeAngle | Slightly increased accuracy using Ensemble; similar in other classifiers
Removing Pedestrian Wait Time | Slightly reduced accuracy using Ensemble; did not affect other classifiers (89.9%) than above
Removing DTCW | Slightly increased accuracy (90.9%) using Ensemble; similar in other classifiers
Removing DTCurb | No Change
Base accuracy = 89.9%

## Slide 37: Feature Selection
Removing Pedestrian average velocity | Slightly decreased accuracy (89%) using Ensemble; similar in other classifiers
Removing GazeRatio | No Change
Removing Gap duration | Decreased accuracy (87% max in Ensemble); more significant reduction in other classifiers
Removing Gap duration
Base accuracy = 89.9%

## Slide 38: Ensemble
Only Gap duration
Normalized

## Slide 39: Ensemble
Only Gaze ratio
Normalized

## Slide 40: SVM – Fine Gaussian
Only Velocity (average)
Normalized

## Slide 41: Ensemble
Only DTCurb
Normalized

## Slide 42: SVM
Only DTCW
Normalized

## Slide 43: SVM
Only Wait Time
Normalized

## Slide 44: Ensemble
Only Gaze Angle
Normalized

## Slide 45: Ensemble
Only Vehicle ID
Normalized

## Slide 46: Ensemble
Only Pedestrian Heading
Normalized

## Slide 47: SVM – Fine Gaussian
Train Data
Gap duration
Average Ped Speed
DT Curb
DT CW
Cumulative Wait

## Slide 48: SVM – Fine Gaussian
Train Data
Gap duration
Average Ped Speed
DT Curb
DT CW

## Slide 49
(a)
(b)

## Slide 50
(a)
(b)

## Slide 51: Behavior measures definitions
Waiting time [s]:
  Time when pedestrian started waiting near the crosswalk till the time they started to walk that ended in them crossing the road.
  Exact definition of waiting time not available in the literature I searched / used for comparison [1] [2].
Crossing speed [m/s] :
  The average speed of pedestrians during crossing (i.e. start of cross till reaching the other side of the road)
  start of cross
    Start walking from wait that leads to a cross (wait to cross)
    Reach the edge of the road (approach to cross)
Gap acceptance:
  Traffic gap [s] is defined as the duration taken by the vehicle to reach the pedestrian.
  In [3], traffic is calculated between two time points: (1) when pedestrian is about to step foot on the road and (2) when the car has crossed the vertical line of pedestrian path
[1] Hamed, M. M. (2001). Analysis of pedestrians’ behavior at pedestrian crossings. Safety science, 38(1), 63-82.
[2] X. Zhuang and C. Wu, “Pedestrians’ crossing behaviors and safety at unmarked roadway in China,” Accid. Anal. Prev., vol. 43, no. 6, pp. 1927–1936, 2011.
[3] G. Yannis, E. Papadimitriou, and A. Theofilatos, “Pedestrian gap acceptance for mid-block street crossing,” Transp. Plan. Technol., vol. 36, no. 5, pp. 450–462, 2013.

## Slide 52: Behavior measures - descriptives
N = 540 crossings (30 subjects, 6 scenarios, 6 crossings)
Measure | Mean | Median | Maximum | Minimum
Waiting Time [s] | 8.95 | 2.1 | 161.1 | 0
Crossing speed [m/s] | 1.68 | 1.70 | 3.29 | 0.40
The very high difference between median and maximum values of the wait times shows that a disproportionately small number of people have high waiting times.

## Slide 53: Behavior measures - histograms
N = 540 crossings (30 subjects, 6 scenarios, 6 crossings)
The very high difference between median and maximum values of the wait times shows that a disproportionately small number of people have high waiting times.

## Slide 54: Waiting time outliers
Participants with high waiting times were discarded.
Outliers calculated from box plot and IQR
Mild outliers -> waiting time > 33.1 s
Extreme outliers -> waiting time > 52.2 s
N = 525 (no extreme outliers)
N = 505 (no mild outliers)

## Slide 55: H-PED Model

## Slide 56: Motivation
Multi-modality

## Slide 57: Related Work

## Slide 58: Research Questions

## Slide 59: Methodology

## Slide 60: Methodology

## Slide 61: Results: Gap parameter Distribution
Total gaps = 2932
There are several high value (X 105) and negative valued gaps, possibly because of small negative values of vehicle to pedestrian distance and small negative values of
Remove negative gaps, gaps with small vehicle velocity (0.5 m/s), N = 2805
Boxplot (Refer Figure)
  Lower limit = 0
  Upper limit = 10.78 s
Remove gaps greater than 10.78 s, N = 2655
  Accepted Gaps = 480
  Rejected Gaps = 2175

## Slide 62: Results: Gap Distribution

## Slide 63: Results: SVM Gap Acceptance
Features (n=9) | Description
F_cumwait | Cumulative wait time [s]
F_pedSpeed | Pedestrian speed in the last one second [m/s]
F_pedVehDist | Distance between pedestrian and vehicle [m]
F_DTCurb | Lateral distance between pedestrian and the curb [m]
F_DTCW | Longitudinal distance between pedestrian and CW [m]
F_Gaze | Proportion of time pedestrian looks at vehicle
F_VehSpeed | Instantaneous vehicle speed [m/s]
F_vehAcc | Instantaneous vehicle acceleration [m/s^2]
F_isSameDirection | (Boolean) Whether pedestrian facing the cars or walking in the same direction as the cars
A gap is accepted when pedestrian starts to cross
Jaywalking gaps are neglected.
Total gaps,
Accepted Gaps, n = 480
Rejected Gaps, n = 2185
80% training
  Accepted Gaps, n = 386
  Rejected Gaps, n = 1746

## Slide 64: Results: SVM Gap Acceptance
Original, Accepted Gaps = 386, Rejected Gaps = 1746
Model Description | Type | Accuracy | Precision | Recall | F1-Score
All 9 features (CV) | SVM (Medium Gaussian) | 0.86 | 0.40 | 0.73 | 0.52
8 features: No ‘VehAcc’ (CV) | SVM (Medium Gaussian) | 0.86 | 0.35 | 0.77 | 0.48
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) | 0.86 | 0.36 | 0.76 | 0.49
CV - 10-fold Cross validation
TS – 20% test set

## Slide 65: Results: SVM Gap Acceptance
BootStrap_1, Accepted Gaps = 2 X 386, Rejected Gaps = 1746
Model Description | Type | Accuracy | Precision | Recall | F1-Score
All 9 features (CV) | SVM (Fine Gaussian) | 0.92 | 0.83 | 0.90 | 0.86
8 features: No ‘VehAcc’ (CV) | SVM (Fine Gaussian) | 0.88 | 0.78 | 0.83 | 0.81
7 features: No Acc, No direction (CV) | SVM (Fine Gaussian) | 0.88 | 0.76 | 0.83 | 0.80
7 features: No Acc, No direction (TS) | SVM (Fine Gaussian) | 0.83 | 0.51 | 0.43 | 0.47
CV - 10-fold Cross validation
TS – 20% test set

## Slide 66: Results: SVM Gap Acceptance
BootStrap_2, Accepted Gaps = 3 X 386, Rejected Gaps = 1746
Model Description | Type | Accuracy | Precision | Recall | F1-Score
All 9 features (CV) | SVM (Fine Gaussian) | 0.95 | 0.95 | 0.92 | 0.93
8 features: No ‘VehAcc’ (CV) | SVM (Fine Gaussian) | 0.91 | 0.92 | 0.87 | 0.89
7 features: No Acc, No direction (CV) | SVM (Fine Gaussian) | 0.91 | 0.91 | 0.88 | 0.89
7 features: No Acc, No direction (TS) | SVM (Fine Gaussian) | 0.81 | 0.45 | 0.45 | 0.45
CV - 10-fold Cross validation
TS – 20% test set

## Slide 67: Results: SVM Gap Acceptance
BootStrap_2, Accepted Gaps = 3 X 386, Rejected Gaps = 1746
Cross-validation results
Removed Feature | Type | Accuracy | Precision | Recall | F1-Score
Veh-Ped distance | SVM (Fine Gaussian) | 0.83 | 0.74 | 0.82 | 0.78
DT Curb | SVM (Fine Gaussian) | 0.84 | 0.83 | 0.78 | 0.80
DT Crosswalk | SVM (Fine Gaussian) | 0.85 | 0.85 | 0.79 | 0.82
Vehicle Speed | SVM (Fine Gaussian) | 0.86 | 0.82 | 0.83 | 0.82
Pedestrian Speed | SVM (Fine Gaussian) | 0.87 | 0.85 | 0.83 | 0.84
Cumulative Wait | SVM (Fine Gaussian) | 0.90 | 0.90 | 0.87 | 0.88
Pedestrian Gaze | SVM (Fine Gaussian) | 0.91 | 0.90 | 0.87 | 0.88

## Slide 68: Results: Gap parameter Distribution (Trial 2)
Total gaps = 2938
There are several high value (X 105) and negative valued gaps, possibly because of small negative values of vehicle to pedestrian distance and small negative values of
Remove negative gaps, gaps with small vehicle velocity (0.5 m/s), N = 2812
Boxplot (Refer Figure)
  Lower limit = 0
  Upper limit = 10.84 s
Remove gaps greater than 10.78 s, N = 2658
  Accepted Gaps = 480
  Rejected Gaps = 2178

## Slide 69: Results: SVM Gap Acceptance (Trial 2)
Features (n=9) | Description
F_cumwait | Cumulative wait time [s]
F_pedSpeed | Pedestrian speed in the last one second [m/s]
F_pedVehDist | Distance between pedestrian and vehicle [m]
F_DTCurb | Lateral distance between pedestrian and the curb [m]
F_DTCW | Longitudinal distance between pedestrian and CW [m]
F_Gaze | Proportion of time pedestrian looks at vehicle
F_VehSpeed | Instantaneous vehicle speed [m/s]
F_vehAcc | Instantaneous vehicle acceleration [m/s^2]
F_isSameDirection | (Boolean) Whether pedestrian facing the cars or walking in the same direction as the cars
F_isEgoNearLane | (Boolean) Whether the ego car is in the near lane or far lane
A gap is accepted when pedestrian starts to cross
Jaywalking gaps are neglected.
Accepted Gaps, n = 480
Rejected Gaps, n = 2178
80% training
  Accepted Gaps, n = 386
  Rejected Gaps, n = 1740

## Slide 70: Results: SVM Gap Acceptance
Original, Accepted Gaps = 386, Rejected Gaps = 1740
Model Description | Type | Accuracy | Precision | Recall | F1-Score
All 10 features (CV) | SVM (Quadratic) | 0.86 | 0.43 | 0.67 | 0.52
9 features: No ‘VehAcc’ (CV) | SVM (Cubic) | 0.84 | 0.46 | 0.57 | 0.51
7 features: No Acc, No direction, No Lane (CV) | SVM (Cubic) | 0.85 | 0.39 | 0.62 | 0.48
CV - 5-fold Cross validation
TS – 20% test set

## Slide 71: Results: SVM Gap Acceptance
BootStrap_1, Accepted Gaps = 2 X 386, Rejected Gaps = 1740
Model Description | Type | Accuracy | Precision | Recall | F1-Score
All 10 features (CV) | SVM (Fine Gaussian) | 0.91 | 0.81 | 0.88 | 0.84
9 features: No ‘VehAcc’ (CV) | SVM (Fine Gaussian) | 0.88 | 0.77 | 0.84 | 0.80
9 features: No Acc, No direction (TS) | SVM (Fine Gaussian) | 0.86 | 0.46 | 0.67 | 0.54
CV - 10-fold Cross validation
TS – 20% test set

## Slide 72: Cross Intent parameter distribution
Total, N = 6009
w/ Intent, N = 4925
w/o intent, N = 1084

## Slide 73: Cross Intent parameter distribution
Only pedestrians with crossing intent data

## Slide 74: Cross Intent parameter distribution
Only pedestrians without crossing intent

## Slide 75: Results: Cross Intent
Features (n=9) | Description
mean_pedSpeed | Pedestrian speed in the observation window [m/s]
mean_pedVehDist | Distance between pedestrian and vehicle [m]
mean_DTCurb | Lateral distance between pedestrian and the curb [m]
mean_DTCW | Longitudinal distance between pedestrian and CW [m]
Gaze | Proportion of time pedestrian looks at vehicle
mean_VehSpeed | Instantaneous vehicle speed [m/s]
mean_vehAcc | Instantaneous vehicle acceleration [m/s^2]
isSameDirection | (Boolean) Whether pedestrian facing the cars or walking in the same direction as the cars
Duration | Proportion of obs. Window for which there is an ego-vehicle
Jaywalking pedestrians are neglected.
80% training

## Slide 76: Results: SVM Cross Intent
Original,
Model Description | Type | Accuracy | Precision (C/NC) | Recall (C/NC) | F1-Score (C/NC)
All 9 features (CV) | SVM (Medium Gaussian) | 0.85 | 0.95/0.36 | 0.87/0.62 | 0.91/0.45
8 features: No ‘VehAcc’ (CV) | SVM (Medium Gaussian) | 0.86 | 0.35 | 0.77 | 0.48
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) | 0.86 | 0.36 | 0.76 | 0.49
CV - 10-fold Cross validation
TS – 20% test set

## Slide 77: Results: Cross Intent (Trial 2) w/o ego car
Features (n=9) | Description
mean_pedSpeed | Pedestrian speed in the observation window [m/s]
mean_DTCurb | Lateral distance between pedestrian and the curb [m]
mean_DTCW | Longitudinal distance between pedestrian and CW [m]
Jaywalking pedestrians are neglected
W/ Cross Intent, n = 12031
W/O Cross Intent, n = 2713
80% training
  W/ Cross Intent, n = 9630
  Rejected Gaps, n = 2165

## Slide 78: Results: SVM Cross Intent
Original,
Model Description | Type | Accuracy | Precision (C/NC) | Recall (C/NC) | F1-Score (C/NC)
All 9 features (CV). No duration | SVM (Fine Gaussian) | 0.85 | 0.96/0.35 | 0.87/0.68 | 0.91/0.46
8 features: No ‘VehAcc’ (CV) | SVM (Medium Gaussian) |  |  |  | 
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) |  |  |  | 
CV - 5-fold Cross validation
TS – 20% test set

## Slide 79: Results: SVM Cross Intent
BootStrapped X 1, Cross Intent = 9630, W/O Cross Intent = 2 X 2165
Model Description | Type | Accuracy | Precision (C/NC) | Recall (C/NC) | F1-Score (C/NC)
All 9 features (CV). No duration | SVM (Medium Gaussian) | 0.80 | 0.89/0.62 | 0.84/0.71 | 0.86/0.66
8 features: No ‘VehAcc’ (CV) | SVM (Fine Gaussian) |  |  |  | 
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) |  |  |  | 
CV - 5-fold Cross validation
TS – 20% test set

## Slide 80: Results: Cross Intent (Trial 2) w/ ego car
Features (n=9) | Description
mean_pedSpeed | Pedestrian speed in the observation window [m/s]
mean_pedVehDist | Distance between pedestrian and vehicle [m]
mean_DTCurb | Lateral distance between pedestrian and the curb [m]
mean_DTCW | Longitudinal distance between pedestrian and CW [m]
Gaze | Proportion of time pedestrian looks at vehicle
mean_VehSpeed | Instantaneous vehicle speed [m/s]
mean_vehAcc | Instantaneous vehicle acceleration [m/s^2]
isSameDirection | (Boolean) Whether pedestrian facing the cars or walking in the same direction as the cars
Duration | Proportion of obs. Window for which there is an ego-vehicle
IsEgoNearLane | (Boolean) Whether the ego car is in the near lane or far lane
Jaywalking pedestrians are neglected
W/ Cross Intent, n = 18749
W/O Cross Intent, n = 3577
80% training
  W/ Cross Intent, n = 15011
  Rejected Gaps, n = 2850

## Slide 81: Results: SVM Cross Intent
Original,
Model Description | Type | Accuracy | Precision (C/NC) | Recall (C/NC) | F1-Score (C/NC)
All 9 features (CV). No duration | SVM (Fine Gaussian) | 0.87 | 0.98/0.27 | 0.88/0.76 | 0.93/0.40
8 features: No ‘VehAcc’ (CV) | SVM (Medium Gaussian) |  |  |  | 
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) |  |  |  | 
CV - 5-fold Cross validation
TS – 20% test set

## Slide 82: Results: SVM Cross Intent
Boot strapped twice
Model Description | Type | Accuracy | Precision (C/NC) | Recall (C/NC) | F1-Score (C/NC)
All 9 features (CV). No duration | SVM (Medium Gaussian) | 0.81 | 0.80/0.84 | 0.90/0.71 | 0.85/0.77
All 9 features (CV). No duration | SVM (Fine Gaussian) | 0.94 | 0.94/0.94 | 0.97/0.91 | 0.96/0.92
7 features: No Acc, No direction (CV) | SVM (Medium Gaussian) |  |  |  | 
CV - 5-fold Cross validation
TS – 20% test set